# Using an Elitech RC5 temperature recorder under Linux
# Prior to starting this, I wish to point out that this apparatus shows a great deal of inertia (I mean that its response to temperature variations is slow, which is likely due to its plasting envelope). While checking a domestic refrigerator temperature moves, I noticed that, while the "Gresinger" control thermometer responded very quikly to temperature changes, RC5 took a lot more time. When bringing it back from inside the fridge (about 5°C) to the room at 22°C, it took more than 20 minutes to settle.
# Testing the connexion of your Elitech module to your computer operating system
# Boot your system, then plug your Elitech RC5 to an usb port.
# Then check wich port it is connected to. The system simulates a serial device, so you are expected to check recent serial connexions :
$ cd /dev
$ ls -lt | more
(which displays a list of devices sorted by time, the newest appearing first)
On my Debian system, I get :
$ ....... ttyUSB0
When you unplug the module, the ttyUSB0 (or whatever else) should no longer show when listing again, it should reappear whenever replugged, which test means that your connexion is OK and tells you which port is concerned.
# Installing the linux driver
# You must now install python 2.7 :
$ sudo apt-get install python
This being done, the following driver is what you need :
elitech-datareader 0.9.5
https://pypi.org/project/elitech-datareader/#files

elitech-datareader-0.9.5.tar.gz

once downloaded, untar the file :

$ tar -xzf elitech-datareader-0.9.5.tar.gz

In the directory elitech-datareader-0.9.5, open the README.txt file and read it. Don't bother about the serial port driver, you don't need it in a linux box, at least not if you are running a recent Debian or Ubuntu distro, as found in the above test of usb/serial port.

Then you must install this from same directory:

$ python setup.py install

You may have to do this operation as :

# python setup.py install

or as :

$ sudo python setup.py install

This being done, you are ready to use your RC5 Ellitech Temperature Recorder

====================================================================

Reading next lines on the README file will teach you how to initialize/re-initialize, configure and use your RC5 Ellitech data recorder. True enough : you must use Xterms to call the commands. However, you won't necessarily have to type these lines of command at each use of the apparatus :

From this document or from others, i.e. the README file, you can easily copy/paste appropriate commands onto an xterm. If you are carrying several test, you may leave the xterm open and recall commands each time.

Here is an example of the 'command set' command that I use to initialize/re-initialize (reset) the module prior to a new use :

root@Debian-Stretch:/home/bd/elitech-datareader-0.9.5# elitech-datareader --command set --interval=60 --upper_limit=60.0 --lower_limit=-30.0 --station_no=1 --stop_button=y --delay=0.0 --tone_set=y --alarm=x --temp_unit=C --temp_calibration=0.1 --dev_num=1234567890 --encode=utf8 /dev/ttyUSB0

You may have noticed that this only works when launched as root... I have not yet spent time to figure out how to operate this as user.

This reset command (-- command set) calls for one measurement per minute (60 sec), in the range betweed 60°C to -30°C, with a calibration correction of 0.1, from serial port /dev/ttyUSB0

Once this command has been launched, unplug the module and press firmly onto the ►button for at least 4 seconds, until the ►icon appears on the display. Then the measurements and recordind start. You may place the module anywhere you want to measure and record temperatures.

After a few hours or days, whenever you decide the measurement is over, bring the module close to the computer and plug it again to same usb port.

Launching the following command :

# elitech-datareader --command get /dev/ttyUSB0

will display the results on screen. If instead you wish to record this on a text file, just do this :

# elitech-datareader --command get /dev/ttyUSB0 > /home/bd/MyRecordsFile.txt

then you recuperate the text file and change owners :

# chown bd MyRecordsFile.txt

then rename it with extension csv :

$ mv MyRecordsFile.txt MyRecordsFile.csv

then open that csv file with libreoffice :

libreoffice MyRecordsFile.csv

chose three columns separators, that is, tab, space and ':' so that you get separated columns for you to work easily. Remove a few first lines and a few last lines, so as to only keep whatever concerns the test proper. You may then extract appropriate information about the test : lower and upper values, gap, averages... and create diagrams etc...